## Slide 1: THE FATE OF METHYLCYCLOHEXANE METHANOL IN SOIL AND EFFECT ON ENZYME ACTIVITY W. Doggett* and F. Eivazi, Department of Agriculture and Environmental Sciences, Lincoln University in Missouri
ABSTRACT
Methylcyclohexane methanol (MCHM) is the chemical that leaked into the Elk River, in Charlestown, West Virginia on the 9th of January, 2014, causing state of emergency called for use of drinking water contaminated with the chemical. Methylcyclohexane methanol is an organic compound classified as a saturated higher alicyclic primary alcohol. It is commonly used in air fresheners and as frothing agent for coal processing and cleaning. The full toxicity of this chemical to humans was unknown at the time of spill and there is still lack of information on exact toxic effects of the crude MCHM. In a recent study it was determined that the MCHM can cause damage to human DNA and potentially cause cancer and reproductive problems. Soils are ultimate recipient of all kinds of contaminates from different sources. There is a need to study and investigate the properties of the MCHM in water and soil especially with the crude MCHM. If released to soil, MCHM is expected to have very high mobility. Volatilization from moist soil surfaces is expected to be an important fate process. To determine toxicity of this chemical on soil biological properties, we measured beta-glucosidase activities in soil treated with different rates and incubated for periods of one hour to 4-weeks. Results indicated that in short term enzyme activity was inhibited by MCHM.
Discussion
Soil enzymatic activities and microbial biomass carbon are considered to be two important soil biological factors affected by contamination. β-glucosidase is involved in the hydrolysis of cellobiose. The sensitivity of this enzyme to changes to the soil conditions, specially the introduction of contaminants makes the activity assay as indicators of microbial activity and often used for assessment of soil quality. There is a need to study and investigate the properties of the MCHM in water and soil especially with the crude MCHM. If released to soil, MCHM is expected to have very high mobility. Volatilization from moist soil surfaces is expected to be an important fate process. We hypothesized that MCHM will inhibit the activity of β-glucosidase which is indication for toxicity of MCHM to microbial community.
MATERIALS AND METHODS
Soil properties: Soil (0-10 cm) collected from the Lincoln University Carver Farm, Cole County, Jefferson City, MO (38◦3136.1N, 92◦822.9W). The physical–chemical properties of the soils studied were determined by standard methods generally used in soil laboratories. The soil used had a pH of 5.8, Organic Matter %3.4, Cation Exchange Capacity 11.7Cmole/Kg; Textural analysis showed 76.6% sand, 16.6% silt loam and 6.6% clay.
Application of Methylcyclohexane methanol (MCHM) : The liquid chemical was applied to the soil and mixed till homogenously distributed. Treatments applied at the rate of 5, 10, 15, and 25 ml/kg of soil. Control did not have any added chemical.
Enzyme Activity: The activity measurement of enzyme, β-glucosidase was carried out by method as described in Eivazi and Tabatabai (1988). β-glucosidase activity was measured based on the colorimetric determination of p-nitrophenol released after incubation of soil amended with p-nitrophenyl- β-D-glucopyranoside as the substrate. All chemicals including the substrate used for determination of enzyme activity were obtained from Sigma Aldrich. Measurements were made in 3 replications.
Statistical analysis: Statistical analysis was carried out using randomized block design. Analysis of Variance was performed using Statistix 8 program at P< 0.05. The Tukey Multiple Comparison test was used to compare the difference in treatment means.
INTRODUCTION
4-methylcyclohexyl-methanol is an organic compound with the formula CH3C6H10CH2OH. Classified as a saturated higher alicyclic primary alcohol. It is colorless oil with a faint mint-like alcohol odor which is only slightly soluble in water but highly soluble in many organic solvents. In the days immediately following January 9, 2014, the West Virginia Poison Center received calls from over 1,900 patients reporting chemical exposures related to the drinking water. Most reported symptoms included mild rashes and reddened skin from dermal exposure, or GI distress (nausea, vomiting and/or diarrhea) from ingesting contaminated water. On January 9, 2014, an estimated 10,000 gallons of an industrial chemical, 4-Methylcyclohexanemethanol (MCHM), spilled into the Elk River just upstream from the Kanawha County municipal water intake in Charleston, West Virginia. This municipal water system serves nearly 300,000 people whose water was affected by the chemical spill. Due to the uncertainty over the chemical levels in the water supply, the Office of the Governor issued a "Do Not Use" order at 6:00 pm on January 9, 2014. Later that evening, the West Virginia Department of Health and Human Resources contacted CDC about the release and requested assistance to review water sampling data and provide a drinking water screening level for MCHM.
Conclusion
The results for β-glucosidase activity measured for the period of one hour up to 4 weeks incubation time ( Figures 1-4) indicated that at short time
one hours incubation, though not statistically significant, but compared to the control the activity was reduced at application rate of 5 ml/kg. For other time periods the activity showed variable results and after 4 weeks enzyme activity increased indication that MCHM probably volatilized from soil and/ or microorganisms are using the MCHM as carbon source and are not adversely affected by the chemical.
Future studies are needed to measure microbial carbon biomass and the variation in microbial species that are affected b this chemical in soil.
Literature Cited
Eivazi, F. and M.A. Tabatabi. 1988. Glucosidase and galactosidase in soils. Soil Biol Biochem Vol. 20 No. 5 –pages 601-608
http://en.wikipedia.org/wiki/4-Methylcyclohexanemethanol.
http://www.technology.org/2014/03/28/tests-elucidate-odor-properties-contaminants-affecting-west-virginia-residents/.
McGuire, Michael J.; Suffet, I.H. (Mel); Rosen, Jeffrey, Consumer Panel Estimates of Odor Thresholds for Crude 4-Methylcyclohexanemethanol, Journal - American Water Works Association, Volume / Number: 106, Number 10, October 2014
RESULTS
Acknowledgement: We wish to express our thanks to the USDA/NIFA Capacity Building Teaching Grant #2013-38820-21449.
Chart: 1-hr Effect of 4-methylcyclohexylmethanol on Glucosidase Enzyme
| 1-hr
5 | 12.96
15 | 26.03
25 | 20.05
Control | 24.38
Chart: 24-hr Effect of 4-methylcyclohexylmethanol on Glucosidase Enzyme
| 24-hr
5 | 9.907
15 | 8.28
25 | 8.67
Control | 10.41
Chart: Week 3 Effect of 4-methylcyclohexylmethanol on Glucosidase Enzyme
| Week 3
5 | 20.2
15 | 20.63
25 | 23.37
Control | 15.99
Chart: Week 4 Effect of 4-methylcyclohexylmethanol on Glucosidase Enzyme
| Week 4
5 | 20.99
15 | 17.41
25 | 15.53
Control | 15.18
Methylcyclohexyl methanol Structure
OBJECTIVE/HYPOTHESIS
To determine toxicity of this chemical on soil biological properties, we measured b-glucosidase activity in soil treated with different rates of MCHM and incubated for periods of one hour to four-weeks.
Yellow color intensity measured in spectrophotometer